## Slide 1
$1.9764/gal
MESP
$1.99/gal
Market price
+1.4¢/gal
Margin
$636.7 M
TCI
$606.3 M
FCI
$35.3 M/yr
Total OPEX
10% / $0
IRR / NPV
✓ MESP (1.9764/gal) < Market(1.99/gal) — Viable at 10% IRR. WA Clean Fuel Standard + D3 RIN credits provide additional upside not in base MESP.
Fig. 2. Sensitivity Analysis — Star (Volcano) Plot
Top 5 variables | Steep slope = high leverage on MESP
Fig. 1. Sensitivity Analysis — Tornado Plot
Base MESP = $1.9764/gal | Market = $1.99/gal | Variables ranked by |Δ MESP|
Chart: Normalized variable value (−1 = low case | 0 = base | +1 = high case)
| -1 (low) | -0.5 | 0 (base) | 0.5 | +1 (high)
Ethanol yield | 1.49 | 1.7332 | 1.9764 | 2.1132 | 2.25
Discount rate (IRR) | 1.88 | 1.9282 | 1.9764 | 2.1782 | 2.38
TCI ±30% | 1.78 | 1.8782 | 1.9764 | 2.0732 | 2.17
OPEX ±20% | 1.86 | 1.9182 | 1.9764 | 2.0332 | 2.09
Plant life | 1.87 | 1.9232 | 1.9764 | 2.0382 | 2.1
Base MESP ($1.9764) | 1.9764 | 1.9764 | 1.9764 | 1.9764 | 1.9764
Market ($1.99) | 1.99 | 1.99 | 1.99 | 1.99 | 1.99
Chart: 
| Electricity price | Retrofit credit | Enzyme cost | Feedstock cost | Feedstock moisture | Plant life | OPEX ±20% | TCI ±30% | Discount rate (IRR) | Ethanol yield
 | 1.95 | 1.95 | 1.94 | 1.94 | 1.93 | 1.87 | 1.86 | 1.78 | 1.88 | 1.49
Favorable → lower MESP | 0.0264 | 0.0264 | 0.0364 | 0.0364 | 0.0464 | 0.1064 | 0.1164 | 0.1964 | 0.0964 | 0.4864
Unfavorable → higher MESP | 0.0136 | 0.0436 | 0.0436 | 0.0436 | 0.0636 | 0.1236 | 0.1136 | 0.1936 | 0.4036 | 0.2736
Δ$0.76
Δ$0.50
Δ$0.39
Δ$0.23
Δ$0.23
Δ$0.11
Δ$0.08
Δ$0.08
Δ$0.07
Δ$0.04
◄ Base $1.9764
Each line swept from low (−1) through base (0) to high (+1). Steeper slope = greater sensitivity. All lines intersect at base MESP. Source: EconAnalysis_Final_v2.docx Table 5 / dw1910a.xlsm AP_SENSITIVITY.
One-at-a-time sensitivity. Δ = total MESP swing. Blue bars = favorable (lower MESP); Orange = unfavorable (higher MESP).
Source: NREL dw1910a.xlsm AP_SENSITIVITY; Humbird et al. (2011) NREL/TP-5100-47764.