## Slide 1
Process Flow Diagram — Pre-1937 Seattle Gas Works Coal Gasification
Aspen Plus V14 Model Core | CHEME 486 Report 2
RYIELD
Decomposition
Mixer
R-101 Conditions
Type: RYIELD
T: 25°C (isothermal)
P: 1.013 bar
Yields: ultimate analysis
R-101
M-101
R-201 Conditions
Type: RGIBBS
T: 1050°C
P: 1.1 bar
Products: 10 species
R-201
S-COAL
7,100 kg/hr
25°C | 1.013 bar
S-DECOMP
7,100 kg/hr | 25°C
S-STEAM
9,000 kg/hr
184°C | 10.3 bar
S-MIX
16,100 kg/hr
91°C | 1.013 bar
RGIBBS
Gasifier
S-RAWGAS
16,100 kg/hr
1050°C | 1.1 bar
17.6%
3,428
5.9%
2,808
0.2%
57
14.89 kg/kmol
S-RAWGAS Equilibrium Composition
Component
Mol %
kg/hr
H₂
47.3%
1,031
CO
28.9%
8,765
Mass Balance Summary
Coal feed (S-COAL): 7,100 kg/hr
Steam feed (S-STEAM): 9,000 kg/hr
Total in: 16,100 kg/hr
Raw gas (S-RAWGAS): 16,100 kg/hr ✓ 0.0%
H₂O
CO₂
N₂
Avg MW
Design Spec: GAS-RATE
Target: 170,000 Nm³/day S-RAWGAS (STDVOL)
Tolerance: ±1,700 Nm³/day (1%)
Vary: S-STEAM flow (4,000–9,000 kg/hr)
Converged: 9,000 kg/hr | Error: −338 Nm³/day ✓
Legend:
R-101 RYIELD (coal decomp.)
M-101 Mixer
R-201 RGIBBS (gasifier)
Coal stream
Steam stream
Gas stream
Property method: PR-BM | Stream class: MIXCINC | Enthalpy: HCOALGEN | Density: DCOALIGT