## Slide 1
Apple pomace transport
Truck delivery from regional cider producers
Pretreatment reactor
Aspen Plus V14: R-201, Steam Explosion, 160 deg C @ 6.18 bar
Solid-liquid separation
FI-201, screw press; liquid hydrolysate forward
Enzymatic hydrolysis
Aspen Plus V14: R-202, cellulase/pectinase, 50 deg C
Fermentation vessels
Aspen Plus V14: R-301, S. cerevisiae, 32 deg C
Beer well
V-301, beer collection and clarification
Beer column
Aspen Plus V14: T-401, stripping column
Molecular sieve dehydration
MS-401, 3A zeolite; >99.5 mol% ethanol
Ethanol storage
TK-401 ★ repurposed gas holders H-401/H-402
Fuel ethanol distribution
Pomace receiving & storage
Y-200, receiving pad; max 24 h inventory
Feed preparation / milling
SR-201, hammermill; 5-10 mm particle size
Legend:
Liquid / slurry stream
Liquid/gas byproduct
Solid feed / byproduct
Aspen model
Hand calc
Storage/output
Transport / receiving
Byproducts
Steam
Enzymes
Yeast
CO₂ vent
Yeast / cell mass
Depleted Pomace (Waste)
Yeast / Cell Mass
Wastewater  WWT
Rectification column
Aspen Plus V14: T-402, rectification column
★ = Unit repurposed from original coal gasification plant
Solid byproduct (depleted pomace)
Gas byproduct (CO₂ vent)